Mountainair Mud Racing

Guideline Manual:

Classes:

Class 1: Unlimited

Class 1 rules: Run whatever your wallet and imagination can come up with.

Engine: Nitrous allowed, Forced induction allowed, any fuel type allowed except for nitro-methane any internal engine modifications allowed, any induction system allowed.

Transmission: Any transmission allowed, must have transmission/scatter shield if using forced induction, nitrous, clutch type coupler, or transbrake.

Tires: Cuts, paddles, tractor tires, any size, must be rubber tires, must be safe, no tire chains allowed

Chassis/Suspension/Body: Must have some type of body, may be fiberglass. Any safe frame allowed, Tube, OEM, or otherwise. 3 and 4 link suspension allowed, OEM ok, Coil-over ok, independent suspension ok, Any engine placement ok except for directly under the driver. Any axle type allowed,

Safety: Roll cages required, driveshaft hoops required for transbrake or clutch type transmission, no tire chains, fire suit required if running Methanol, Nitrous, or Forced Induction, Headers may not point directly at crowd unless it is a full exhaust system, fire extinguisher required, must have firewall, battery must be secured, minimum 5 point racing harness required.

Entry Fee: $70 entry fee w/ 90% payback for top 3 places, unless under 5 vehicles. If under 5 60/40 split. If under 3 then 90% to 1st.

Class 2: Modified / Altered

Class 2 rules: This class is for basically a Class 1 vehicle, with no nitrous, or forced induction.

Engine: No Nitrous or Forced induction. Any internal engine modifications allowed, any heads, blocks, and any induction, any carbs, any fuel injection, or otherwise.

Transmission: Any transmission allowed, must have transmission/scatter shield if using clutch type coupler, or transbrake.

Tires: Cuts, paddles, tractor tires, any size, must be rubber tires, must be safe, no tire chains allowed

Chassis/Suspension/Body: Must have some type of body, may be fiberglass, Any safe frame allowed, Tube, OEM, or otherwise. 3 and 4 link suspension allowed, OEM ok, Coil-over ok, independent suspension ok, Any engine placement ok except for directly under the driver. Any axle type allowed,

Safety: Roll cages required, driveshaft hoops required for transbrake or clutch type transmission, no tire chains, fire suit required if running Methanol, Headers may not point directly at crowd unless it is a full exhaust system, fire extinguisher required, must have firewall, battery must be secured, minimum 5 point racing harness required.

Entry Fee: $60 entry fee w/ 90% payback for top 3 places, unless under 5 vehicles. If under 5 60/40 split. If under 3 then 90% to 1st.

Class 3: Dot 40-54” Uncut

Class 3 rules: This class is for OEM Frames and uncut DOT tires.

Engine: No Nitrous, No forced induction (except diesel, or factory equipped), Methanol allowed with proper safety equipment, Race Fuel ok. Big Blocks limited to 572CI, Small Blocks limited to 454CI. Any internal modifications allowed. Aftermarket heads, blocks, cranks, etc ok. Dual Carbs ok, aftermarket fuel injection ok, any ignition system ok,

Transmission: OEM Style Transmissions only, may be aftermarket. Powerglides ok, Any size or stall torque converter allowed, Transmission brakes and linelocks allowed.

Tires: 40 – 54” DOT Uncut

Body and Chassis: Must be stock appearing body, OEM frames, 4 link and coil-over suspensions ok. Suspension must be safe I.E. no front lift blocks. Engine must be in stock location for vehicle, I.E. underneath the hood. Front engine based vehicles only, mid engine ok in Van’s in stock location. Engine swaps ok. Frame extensions only allowed for suspension mounts, Axle centerline to matchup with fender centerline within 4”. Body swaps allowed, must be safe.

Safety: Driveshaft hoops and or transmission shield recommended if equipped with transbrake or clutch type transmission. Chain Drives allowed. Gutting ok must be based on OEM body. Fiberglass ok on hoods and fenders only. Any exhaust allowed, must not point towards the side, unless full exhaust. Fire extinguisher recommended, must have firewall, battery must be secured, minimum 5 point racing harness recommended. Roll cages recommended, and are required if vehicle is gutted or open top.

Entry Fee: $50 entry fee w/ 90% payback for top 3 places, unless under 5 vehicles. If under 5 60/40 split. If under 3 then 90% to 1st.

Class “Outlaw 4”:

Class “Outlaw 4” rules: This class is for full weight vehicles, OEM frames, OEM type suspensions.

Engine: Engine rules:Nitrous Allowed, Superchargers Allowed, Turbo’s Allowed. Methanol allowed with proper racing equipment (See safety section), E85 ok. Race fuel ok. Dual Carbs allowed, Aftermarket Injection allowed, Aftermarket Head ok, OEM Blocks only. Tunnel Ram ok, any ignition system ok.

Transmission: OEM Style Transmissions only. 9” torque converter max, transbrake and linelocks ok.

Tires: Any size up to 52” Must be rubber. Cuts ok, Tractor tires ok, Paddles ok.

Body and Chassis: Must be full and stock appearing body. OEM frames only, OEM suspension type recommended, solid axle conversion ok, Body swaps allowed, engine swaps allowed. Engine must be in stock location for vehicle, I.E. underneath the hood. Mid Engine ok in stock location (vans) Frame extensions only allowed for suspension mounts, Axle centerline to matchup with fender centerline within 3”.

Safety: Open headers allowed must not point at crowd, no gutting of body, only cutting allowed for tire clearance. Must have safety belt, aftermarket preferred, battery must be secured. If running Methanol, and or Nitrous requires Fire resistant suit, gloves, fire suppression equipment. Roll Cage highly recommended.

Entry Fee: $50 entry fee w/ 90% payback for top 3 places, unless under 5 vehicles. If under 5 60/40 split. If under 3 then 90% to 1st.

Class 4: Dot 38-44” DOT Uncut

Class 4 rules: This class is for full weight vehicles, OEM frames, OEM type suspensions.

Engine: Engine limits. 434 CI small block, 509 CI big block. No nitrous, no forced induction, (Except diesel, single turbo only, or otherwise factory equipped) Methanol allowed with proper racing equipment (See safety section), E85 ok. Race fuel ok. Single carb only, Aftermarket Head ok if street performance replacement I.E. Edelbrock RPM or similar, OEM Blocks only. Tunnel Ram ok if single carb, any ignition system ok.

Transmission: OEM Style Transmissions only. 9” torque converter max, transbrake and linelocks ok.

Tires: 38 to 44” DOT uncut

Body and Chassis: Must be full and stock appearing body. OEM frames only, OEM suspension type recommended, solid axle conversion ok, Body swaps allowed, engine swaps allowed. Engine must be in stock location for vehicle, I.E. underneath the hood. Mid Engine ok in stock location (vans) Frame extensions only allowed for suspension mounts, Axle centerline to matchup with fender centerline within 3”.

Safety: Open headers allowed must not point at crowd, no gutting of body, only cutting allowed for tire clearance. Must have safety belt, aftermarket preferred, battery must be secured. If running Methanol, requires Fire resistant suit, gloves, fire suppression equipment.  If there is an issue brought up about vehicle, it automatically goes before competitors in drivers meeting. If majority agree to leave you in this class, you will stay, if not you will be bumped up to Class 3. Roll cage required on open top.

Entry Fee: $50 entry fee w/ 90% payback for top 3 places, unless under 5 vehicles. If under 5 60/40 split. If under 3 then 90% to 1st.

Class 5: Dot up to 37” Uncut

Class 5 rules: This class is set up for a vehicle which could be driven on the street.

Engine: Must run pump gas or diesel. Single carb or factory EFI only, No nitrous or blowers (Except factory diesel or otherwise factory production). Open headers allowed. Engine size limited to 408 CI small block 474 CI big block (except factory 502, V10 Mopar, or Cadillac 500) OEM Blocks and Heads only, aftermarket ignition systems ok. Carburetion 750 cfm max.

Transmission: OEM only, 10” torque converter max, no transbrakes, linelocks etc. RPM staging limiter ok.

Tires: Up to 37” DOT Uncut

Chassis/Body: Must be full and stock body and frame, OEM suspension type only, solid axle conversion ok, engine swaps allowed within reason. NO BIG BLOCKS IN MINITRUCK, EARLY BRONCO, S-10’s, RANGERS, SAMURI’s, or any of the many other types of small vehicles. Big Blocks ok in ½ ton pickups, Blazers, Fullsize Broncos, Ramchargers, Etc. If vehicle is pushing limits of class, it automatically goes before Tech Manager. Tech Manager will determine whether vehicle is eligible for Class 5, or will be bumped one spot to Class 4. Safety: Open exhaust allowed. Battery must be secured, Seatbelt required. Roll bar required on open top.

*Example of vehicle pushing limits of class: Jeep Wrangler with a big small block 383+CI, and 37” Boggers / Swampers.

*Example of vehicle not pushing limits of class: Mini truck with a small block 350 CI, and 35” Mud Terrains.

Entry Fee: $50 entry fee w/ 90% payback for top 3 places, unless under 5 vehicles. If under 5 60/40 split. If under 3 then 90% to 1st.

Class 6: Any DOT approved Tire which fits rules

Class 6 rules: This shall be known as the Junk Yard class.

Engine: Must run pump gasoline, LPG, or CNG fuels only (no additives, no cover scents, no dyes). Any engine to frame to body combination allowed. Carburetors limited to 1 carb, 700 cfm max, double pumpers ok. Any combination of carburetor spacers or adapters allowed, must not exceed 3”. OEM casting Heads and Blocks. Dual Plane factory cast iron or Aluminum OEM replacement dual plane intakes only.  Stamped steel or cast iron rocker arms only (no Roller rockers).  Tech person will go over engine entirely, if you want in this class you will submit to vacuum test, compression test, or any other test to prove the engine is stock or near stock configuration. No aftermarket ignition allowed, must be points or factory CDI/HEI. Any exhaust allowed Open Headers must not point towards crowd.

Transmission: Any OEM transmission allowed. No hi-stall converters allowed. 11” factory minimum diameter.

Tires: Any size DOT tire allowed, tread depth not to exceed ½” for tires of 35” or over. Tires under 35” allowed no matter what tread depth so long as they are DOT approved. No grooved or intentionally altered tires.

Chassis/Body: Any Body, must cover driver on sides, open top ok, Any frame, axle, and suspension combo you can put together, must be safe. Any engine placement allowed, except for directly under driver. Store Bought lift kits allowed, but discouraged. Shocks recommended. 3 and 4 link suspension, radius suspension allowed, coils and elliptical leaves allowed. Coil-over’s not allowed unless factory struts. Lincoln lockers preferred as traction aiding devices.

Safety: Battery must be secured, Seatbelt Required, Roll Bar required on open top, Must have firewall between driver and engine. Any issue brought up with safety will make vehicle inoperable until violations corrected.

Further Rules / Quirks: **Class 6 participants can protest other competitor vehicles. The rules for protest are 1: a $250 deposit will be required for a protest. Both you and the person you are protesting will pull side by side, and a full tech inspection will be conducted on both vehicles. This inspection will check compression on all cylinders (all cylinders will be averaged, and must come in at 140psi or less averaged), check fuel type, a carb inspection, an ignition inspection, and a random rocker-arm cover will be taken off to inspect rocker arms, and verify casting numbers. If you are found to be correct, you get the $250 back and if before the race other vehicle will be classed accordingly, if after the race, the vehicle will forfeit any prize money. And have to pass full tech inspection before next race. If YOU are found to be in violation of rules, you will lose $250, give up any prize money from the race, and will be exiled from Class 6 permanently. If for some reason, vehicle doesn’t qualify for class upon pre inspection, in regards to engine, there are several options. Option 1: Run in whatever class vehicle fits and upgrade where needed. Option 2: Driver may opt to remove #1 spark plug wire for 1 race, and get a worse motor before the next race. Option 3: Driver may opt to disconnect secondary of a 4 barrel carb if over 700 CFM, (Excluding Dominator and Predator). If a tire issue, it will be brought up for a vote at driver’s meeting. If agreed that you stay in class 6, then you stay, if not you will move up to class the vehicle fits.

Entry Fee: $20 entry fee w/ 90% payback for top 3 places, unless under 5 vehicles. If under 5 60/40 split. If under 3 then 90% to 1st.

The 10% withholding of the entry fees, will be paid to the winner of the Marauder Challenge.

Marauder Challenge rules: Any truck or class of truck is eligible to participate in a triathlon. The vehicles will be competing in the following three events. 1: Standard Mud Bog. 2: Hill and Hole mud pit. 3: Barrel Race. The winner will be based on a points system. The points will be determined on the amount of trucks in the class. I.E. if there are 5 trucks participating in the Challenge 1st place will receive 5 points per event. In this case a total of 15 points is possible if every event (Mud Pit, Hill n Hole, and Barrel Race) is won by the same truck.